## Slide 1
Hooke’s law
Robert Hooke, in 1676, noted that for a spring, the extension was proportional to the load.
It is now more generally stated that in certain cases, the extension (Δx) is proportional to the load (F).

## Slide 2
Hooke’s law
Hooke’s law holds true in some cases of:
Tensile forces (stretching forces)
and in some cases of
Compressive forces (squashing forces)

## Slide 3
Hooke’s law
The constant of proportionality (k) is called the spring constant.

## Slide 4
Hooke’s law
Rearranging the equation we get:
So the units will be:
N m-1
Or
N/m

## Slide 5
Hooke’s law
Example 1
A spring has a spring constant, k, of 10 Ncm-1.
What will the extension be for a load of 50 N?

## Slide 6
Hooke’s law
Example 2
A spring has a spring constant, k, of 5 Ncm-1.
What load will cause it to stretch by 15 cm?

## Slide 7
Hooke’s law
Example 3
A spring stretches 12 cm under a load of 36 N.
What is the spring constant of the spring?

## Slide 8
Hooke’s law
Example 4
An unloaded spring is 12 cm long. If a weight of 15N is hung on the end of it, it extends to 18 cm long.
How long will the spring be, if a weight of 7.5 N is hung on it?
Using information from the first paragraph of the question we get:
Note Δx, is:
18 -12 = 6 cm

## Slide 9
Hooke’s law
Example 4
An unloaded spring is 12 cm long. If a weight of 15N is hung on the end of it, it extends to 18 cm long.
How long will the spring be, if a weight of 7.5 N is hung on it?
Now using the information from the second paragraph:
So the length of the spring will be:
The original length + the extension

## Slide 10
Hooke’s law
AS PHYSICS
Example 5
An aircraft is loaded with 100 kg of fuel. The compression oleos on the undercarriage undergo a compression of 2.5 mm.
What will the additional compression be, if the aircraft then takes on passengers of mass 250 kg?
You can solve this problem using equations, as we have done in the previous questions and if you are happiest doing it that way, then carry on.
However, we can solve the problem just using proportionality.
Oleo

## Slide 11
Hooke’s law
AS PHYSICS
Example 5
An aircraft is loaded with 100 kg of fuel. The compression oleos on the undercarriage undergo a compression of 2.5 mm.
What will the additional compression be, if the aircraft then takes on passengers of mass 250 kg?
100 kg causes a compression of 2.5 mm
So 1 kg will cause a compression of 2.5 mm / 100
So 250 kg will cause a compression of (2.5 mm / 100) x 250
Oleo
Additional compression is 6.25 mm
Note that the total compression is 2.5 mm + 6.25 mm = 8.75 mm

## Slide 12
Hooke’s law
AS PHYSICS
Example 6
What assumption have you made in each of these examples?
That the substances all obey Hooke’s law.
Note that particularly for small extensions, there are many materials that obey Hooke’s law.
This is due to the nature of the intermolecular forces within the materials.
Separation
Force

## Slide 13
Hooke’s law
AS PHYSICS
Example 6
What assumption have you made in each of these examples?
That the substances all obey Hooke’s law.
This area represents the atoms or molecules being pushed together.
There is a repulsive force between them.
Separation
Force

## Slide 14
Hooke’s law
AS PHYSICS
Example 6
What assumption have you made in each of these examples?
That the substances all obey Hooke’s law.
This area represents the atoms or molecules being pulled apart.
There is a force of attraction between them.
Separation
Force

## Slide 15
Hooke’s law
AS PHYSICS
Example 6
What assumption have you made in each of these examples?
That the substances all obey Hooke’s law.
At this point, there is no force so this is the equilibrium position.
Separation
Force

## Slide 16
Hooke’s law
AS PHYSICS
Example 6
What assumption have you made in each of these examples?
That the substances all obey Hooke’s law.
Small displacements around this position are on a part of the curve which is almost straight.
This is the origin of Hooke’s law and the straight line graph that we get from it.
Separation
Force